## Slide 1: Retroffiting existing Combined Cycle Gas Turbines with Post-Combustion Carbon Capture: carbon capture energy penalty reduction
Antoine Verhaeghe
antoine.verhaeghe@umons.ac.be
ETN Webinar – 06/12/24

## Slide 2
CCGT plants will continue to play a significant role in the next decades
Chart: Starting year
| 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042
Operating | 0.831 | 1.4214 | 1.3783 | 4.11 | 1.9333 | 1.986 | 3.3495 | 6.027 | 10.219 | 13.9288 | 10.8524 | 14.837 | 17.18 | 19.55 | 18.8937 | 28.1146 | 36.0673 | 66.4628 | 69.7143 | 37.342 | 29.6804 | 30.997 | 31.677 | 32.0287 | 37.6782 | 42.5801 | 35.7165 | 40.4651 | 48.2466 | 68.0866 | 38.9217 | 36.613 | 46.1084 | 67.622 | 48.4038 | 39.8772 | 30.1117 | 36.7532 | 36.526 | 0.263 | 0.1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Construction | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2.043 | 9.056 | 69.1937 | 32.482 | 12.8632 | 4.584 | 0 | 0 | 0 | 0 | 0 | 0 | 1.56 | 0 | 0 | 0.9 | 0 | 0 | 0 | 0 | 0
Pre-construction | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1.15 | 32.731 | 35.597 | 20.137 | 17.904 | 8.5294 | 7.475 | 14.31 | 2.55 | 0.885 | 0.6 | 0 | 0.7 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Announced | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.7 | 8.334 | 8.115 | 14.752 | 12.343 | 7.967 | 4 | 14.7594 | 0.6 | 0.55 | 0 | 3.31 | 2.3694 | 1.21 | 0.6 | 1.06 | 0 | 0 | 1.8 | 0.4

## Slide 3
  Post-Combustion
  Carbon Capture
  E-fuels
Post-combustion carbon capture is the best option to retrofit existing assets
NOT YET READY

## Slide 4
The amine(s)-based carbon capture process is energy intensive
Stripper
Heat
Absorber
1-5 vol.% CO2
Efficiency ?

## Slide 5: Applying carbon capture to gas turbines is challenging
Mainly part-load operation
Increased transient phases (start-up, shut-down, load variation)
Gas turbines are not ideal for carbon capture application
Low CO2 content in flue gases (4-5 vol.%)
Large flue gas flow rate (6900 m3/s for 500 MWe)
Gas turbines are increasingly used as peaking units

## Slide 6
Research questions
To what extent applying carbon capture penalizes plant performance and flexibility ?
How to reduce the carbon capture energy penalty?

## Slide 7
Research questions
To what extent applying carbon capture penalizes plant performance and flexibility ?
How to reduce the carbon capture energy penalty?

## Slide 8: A conventional 580 MWe CCGT plant has been studied
Gas turbine
Steam cycle
Heat recovery steam generator
ηel = 60.7 %
Pel = 580 MW

## Slide 9
CCGT
CCGT
Carbon capture
What is the carbon capture penalty on the CCGT ?
4.6% CO2
4.6% CO2
560 MWe
- 90% CO2
Heat
Electricity

## Slide 10
The carbon capture plant has been designed and modelled for the CCGT application
 | Absorber | Stripper
Diameter (m) | 18 | 8.5
Packed height (m) | 30 | 30
Stripper
Absorber

## Slide 11
CCGT
CCGT
Carbon capture
-13.5% in efficiency with carbon capture
4.6% CO2
4.6% CO2
560 MWe
MEA

## Slide 12
Chart: 
| RSS
CCGT | 1.64 | 1.71 | 1.86
CCGT+CC | 2.12 | 2.22 | 2.44
CC energy penalty | 0.48 | 0.51 | 0.58
The CCGT performance without/with CC were assessed for different GT loads
Plant load
Energy input [kWh/kWhe]
1.64
100%
2.75
3.07
1.71
75%
50%
1.86
2.12
2.22
2.44
0.48
0.51
0.58

## Slide 13
Chart: 
| RSS
CCGT | 1.64 | 1.71 | 1.86
CCGT+CC | 2.12 | 2.22 | 2.44
CC energy penalty | 0.48 | 0.51 | 0.58
Adding a carbon capture unit reduces significantly plant performance
Energy input [kWh/kWhe]
1.64
100%
2.75
3.07
1.71
75%
50%
1.86
2.12
2.22
2.44
0.48
0.51
0.58
Plant load

## Slide 14
Chart: 
| RSS
CCGT | 1.64 | 1.71 | 1.86
CCGT+CC | 2.12 | 2.22 | 2.44
CC energy penalty | 0.48 | 0.51 | 0.58
Part-load operation increases the CC energy penalty
Energy input [kWh/kWhe]
1.64
100%
2.75
3.07
1.71
75%
50%
1.86
2.12
2.22
2.44
0.48
0.51
0.58
+6.3%
+20.8%
Plant load

## Slide 15
Research questions
To what extent applying carbon capture penalizes plant performance and flexibility ?
How to reduce the carbon capture energy penalty?

## Slide 16
How to reduce the carbon capture penalty?
CCGT
Carbon capture
Performing Exhaust Gas Recirculation (EGR) on the mGT
Improvement of the carbon capture process (solvent, configuration)
Energy integration between the mGT and the CC plant

## Slide 17
How to reduce the carbon capture penalty?
CCGT
Carbon capture
Performing Exhaust Gas Recirculation (EGR) on the mGT
Improvement of the carbon capture process (solvent, configuration)
Energy integration between the mGT and the CC plant
CO2

## Slide 18
How to reduce the carbon capture penalty?
CCGT
Carbon capture
Performing Exhaust Gas Recirculation (EGR) on the CCGT
Improvement of the carbon capture process (solvent, configuration)
Energy integration between the mGT and the CC plant
EGR
CO2

## Slide 19: An EGR loop has been added to the CCGT model
EGR ratio = 35%

## Slide 20
Applying EGR allows to reduce the size and the cost of the carbon capture unit
 | Absorber | Stripper
Diameter (m) | 18 15 | 8.5 8
Packed height (m) | 30 | 30
Stripper
Absorber

## Slide 21
How to reduce the carbon capture penalty?
CCGT
Performing Exhaust Gas Recirculation (EGR) on the CCGT
Improvement of the carbon capture process (solvent, configuration)
Energy integration between the mGT and the CC plant
35% EGR
7.1 vol.% CO2
Carbon capture

## Slide 22
How to reduce the carbon capture penalty?
CCGT
Performing Exhaust Gas Recirculation (EGR) on the CC
GT
Improvement of the carbon capture process (solvent, configuration)
Energy integration between the mGT and the CC plant
35% EGR
7.1 vol.% CO2
Carbon capture
Heat
Electricity

## Slide 23
How to reduce the carbon capture penalty?
CCGT
Performing Exhaust Gas Recirculation (EGR) on the CCGT
Improvement of the carbon capture process (solvent, configuration)
Energy integration between the mGT and the CC plant
35% EGR
7.1 vol.% CO2
Carbon capture
MEA
MDEA/PZ

## Slide 24: The reboiler duty is lower using MDEA/PZ instead of MEA
Reboiler duty [MWth]
Stripper pressure [bar]
MEA
MDEA/PZ
Qreboiler
Stripper
Absorber

## Slide 25
How to reduce the carbon capture penalty?
CCGT
Performing Exhaust Gas Recirculation (EGR) on the CCGT
Improvement of the carbon capture process (solvent, configuration)
Energy integration between the CCGT and the CC plant
35% EGR
7.1 vol.% CO2
Carbon capture
Steam
MEA
MDEA/PZ

## Slide 26: Steam is extracted from the IP/LP crossover to supply heat to the reboiler
278.3°C
3.8 bar

## Slide 27
CCGT
CCGT
Carbon capture
MEA
The CC penalty is reduced from 13.5 to 6.8 abs.% by performing EGR and extracting steam
4.6% CO2
4.6% CO2
560 MWe
CCGT
Carbon capture
35% EGR
7.1% CO2
Steam
MEA

## Slide 28
CCGT
CCGT
Carbon capture
MEA
The CC penalty can be further reduced by 0.5 abs.% by replacing MEA with MDEA/PZ
4.6% CO2
4.6% CO2
560 MWe
CCGT
Carbon capture
35% EGR
7.1% CO2
Steam
MEA
MDEA/PZ

## Slide 29
Conclusions
Implementing CC to CCGTs without adaptations strongly degrades plant performance, and even more during part-load operations
The negative impact can be strongly reduced through some adaptations without modifying existing components of the plant
By performing EGR and extracting steam, the energy penalty is reduced from 13.5 abs.% to 6.8 abs.% using MEA
Replacing MEA with MDEA/PZ results in a CCGT efficiency increase of 0.5 abs.%
Further investigations on part-load and transient operations are required
A techno-economic analysis is required to assess the viability of theses adaptations

## Slide 30: Retroffiting existing Combined Cycle Gas Turbines with Post-Combustion Carbon Capture: carbon capture energy penalty reduction
Antoine Verhaeghe
antoine.verhaeghe@umons.ac.be
ETN Webinar – 06/12/24