## Slide 1
Advancing CO2 Capture –
RWE Cutting-Edge Research for Real-World Solutions
ETN CCS Webinar Series 06th February 2025
Dr. Sandra Schmidt RWE Power AG

## Slide 2
CO2 Capture – Solid knowledge base at RWE 19 years active participation in CO2 Post-combustion Capture Pilot and Demonstration Projects
Shell’s Cansolv Aberthaw UK
BASF‘s OASE® blue Niederaussem Germany
Alstom‘s Chilled Ammonia Mountaineer USA
Alstom‘s Chilled Ammonia USA
CASTOR/ CESAR Esbjerg, Denmark
100,000 operating hours
2005
2006
2007
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
2025
2026
Today >115,000 operating hours
06.02.2025
Advancing CO2 Capture – RWE Cutting-Edge Research for Real-World Solutions, Sandra Schmidt, RWE Power
24/7 longtime operation under real operating conditions
OASE® blue
>55,000 h
CESAR1
>49,000 h
MEA
>18,000 h

## Slide 3
Post-Combustion Capture at RWE’s Innovation Center
Highest capture rates
Solvent management and CO2 quality
Emission mitigation and CO2 quality
Solvent management
All aspects of CCUS
Power plant
Flue gas, raw lignite
WTA®
Flue gas, dry lignite
Dust
SO2/SO3
REAplus
Wet ESP
conventional FGD
Raw lignite
HOK®
Flue gas treatment
CO2 utilisation
CO2 capture
CO2 liquefaction
06.02.2025
Advancing CO2 Capture – RWE Cutting-Edge Research for Real-World Solutions, Sandra Schmidt, RWE Power

## Slide 4
1,550 m3N/h flue gas flow
7.2 tCO2/day CO2 product
90% CO2 capture rate
97% availability
First PCC pilot plant commissioned in Germany
Instrumentation: 285 online measurements
24/7 operation
Post-Combustion Capture Pilot Plant at Niederaussem Evaluation of the process performance needs longtime testing with real flue gas
FGD: Flue gas desulphurization
WESP: Wet electrostatic precipitator
DCC: Direct contact cooler
06.02.2025
Advancing CO2 Capture – RWE Cutting-Edge Research for Real-World Solutions, Sandra Schmidt, RWE Power

## Slide 5
– Membrane-assisted Dissolved Oxygen Removal from Amine solution for CO2 capture
  Goals:
  90% O2-reduction in the solvent
  50% reduction of the degradation rate
  Reduction of the O2–concentration in the CO2 product to <10 ppm
Reduction of the O2-concentration in the solvent means the reduction of:
  solvent degradation, make-up demand
  solvent flow
  corrosion
  effort for CO2 purification
Membrane
Contractor
Single Hollow Fibre
06.02.2025
Advancing CO2 Capture – RWE Cutting-Edge Research for Real-World Solutions, Sandra Schmidt, RWE Power

## Slide 6
– Deep Removal of CO2 and InnoVative Electrification concepts
Negative CO2 emissions by highest capture rates at amine-based capture plants and by electrochemical technologies (pH swing)
2024
X
First results:
CO2 content in the CO2-lean flue gas less than ambient air achieved
321 ppmv @ only 30% higher energy demand
99.8% capture rate
-100 ppm
06.02.2025
Advancing CO2 Capture – RWE Cutting-Edge Research for Real-World Solutions, Sandra Schmidt, RWE Power

## Slide 7
SCOPE – Sustainable OPEration of post-combustion Capture plants Providing facts to the discussion on BAT from 24/7 longtime testing
Testing of emission mitigation technologies
Effects of solvent aging at capture rates of 90-98%
tests on dynamic and start/stop behaviour
Validation of simulation tools (ASPEN, ProTreat, ML)
Mimicked off-gas of natural gas fired plants (CO2 4%, O2 15%)
Hengelo
Waste-to Engergy 500 kg CO2/h
Niederaußem
Lignite 300 kg CO2/h
Tiller CO2 Lab
Biomass, propane 30-40 kg CO2/h
Alkmaar
Waste-to Energy 540 kg CO2/h
Tuticorin
Chemicals
7.500 kg CO2/h
Vindyachal
Hard coal 830 kg CO2/h
Demonstration and holistic analysis of emission management technologies at Niederaussem
Pre-treatment
Emissions control
Emissions monitoring
Atmospheric chemistry
Biodegradation
Testing - Measurement - Modeling of Emissions and Dispersion - Effects - Acceptance
06.02.2025
Advancing CO2 Capture – RWE Cutting-Edge Research for Real-World Solutions, Sandra Schmidt, RWE Power

## Slide 8
Test of emission mitigation technologies for CESAR1 at Niederaussem
Flue gas source: 1,000 MW lignite-fired power plant
Operation mode: 24/7, 300 kgCO2/h@90% capture rate,
Solvent: CESAR1
Test campaigns with more than 20 configurations of emission mitigation technologies: water wash, double water wash, acid wash, dry bed (OASE aerozone®), pretreatment.
c
wash
Acid wash / Double water
c
Water wash
Dry bed
DCC/Pre-Scrubber
WESP
Pretreatment
Pretreatment
ELPI+
FTIR
AMP: 2-amino-2-methylpropan-1-ol
PZ: piperazine
WESP on aerosol-based emissions particle concentration  2 x 106 #/cm³
WESP off volatile emissions particle concentration  2 x 104 #/cm³
06.02.2025
Advancing CO2 Capture – RWE Cutting-Edge Research for Real-World Solutions, Sandra Schmidt, RWE Power

## Slide 9
Effects of high capture rates and of CO2/O2 content in the flue gas
For CESAR1 only small effects of the capture rate on emissions; changes of the CO2/O2 concentration affect the temperature profile in the absorber and emissions
(Proprietary) emission mitigation technologies are available to control emissions regardless of the capture rate and the O2 content in the flue gas
Page 9
Capture rate
CO2~15%
CO2~5%
06.02.2025
Advancing CO2 Capture – RWE Cutting-Edge Research for Real-World Solutions, Sandra Schmidt, RWE Power

## Slide 10
Solid particles in the flue gas with diameter <100 nm can cause aerosol formation
(Proprietary) emission mitigation technologies are available to control emissions regardless of the particle number concentration and size distribution
Emission management
Aerosol and vapor-based emissions – solvent CESAR1
06.02.2025
Advancing CO2 Capture – RWE Cutting-Edge Research for Real-World Solutions, Sandra Schmidt, RWE Power

## Slide 11
Dynamic operation of CO2 capture plants
Load changes, Start/Stop behaviour – not only important for capture rate and thermodynamics, but also regarding emissions
Until now, the dynamic behaviour of capture plants cannot be simulated. But real-world data are available for model validation and for the prognosis of trends.
06.02.2025
Advancing CO2 Capture – RWE Cutting-Edge Research for Real-World Solutions, Sandra Schmidt, RWE Power

## Slide 12
The Post-Combustion Capture Project at Knapsacker Hügel I From R&D to use
Flue gas from sewage sludge combustion
2 x 96,000 tCO2/a (2 x 288 tCO2/day) CO2 product
95% CO2 capture rate
8,000 h/a in operation
Specific energy demand: ≤ 3.0 GJ/tCO2
CO2 transport to storage site: train, ship
CO2 usage projects under discussion
Page 12
06.02.2025
Advancing CO2 Capture – RWE Cutting-Edge Research for Real-World Solutions, Sandra Schmidt, RWE Power

## Slide 13
The Post-Combustion Capture Project at Knapsacker Hügel II From R&D to use
Absorber with approved 3-step purification for the CO2-lean flue gas
Stable and highly efficient solvent
Optimized emission mitigation technology
Low specific energy demand because of solvent and process optimizations
Optimized solvent and water management to minimize solvent loss and waste water
Page 13
06.02.2025
Advancing CO2 Capture – RWE Cutting-Edge Research for Real-World Solutions, Sandra Schmidt, RWE Power

## Slide 14
Page 14
Project development, Design, Funding, Permitting, Construction, Commissioning
Mitigation of Wastes and Emissions, Health & Safety & Environment
Process chain, Plant configuration, Integration, Operation, Measurement technologies
CO2
€
De-Risking and Minimisation of CAPEX and OPEX, Use of Synergies
Consultancy and Supporting Work for RWE’s BECCUS projects (Technology Provider, Authorities, Networks)
Solvent Management
Conclusion
Experience of more than 115,000 operating hours of the CO2 capture pilot plant at Niederaussem and 20 years of CCUS projects
06.02.2025
Advancing CO2 Capture – RWE Cutting-Edge Research for Real-World Solutions, Sandra Schmidt, RWE Power

## Slide 15
Acknowledgements
ACT SCOPE Project No 327341 This project has received funding from RVO (NL), FZJ/PTJ (DE), RCN (NO), BEIS (UK), DST (IN), and DOE (USA) through the ACZ initiative. www.scope-act.org
ACT MeDORA This project has received funding from The RCN (no 308765), FZJ/PTJ (no 03EE5160) and PPS-toeslag TKI-Energie (TKI 2023 MeDORA, program: Nieuw Gas/CCS) www.sintef.no/en/ projects/2023/medora-membrane-assisted-dissolved- oxygenremoval-from-amine-solution-for-co2-capture/
DRIVE This Project has been funded by partners of the CETpartnership (https://cetpartnership.eu) and FZJ/PTJ-MWIKE (no EFO-0216), https://DRIVE-co2.eu/
This project has received funding from the European Union‘s Horizon 2020 research and innovation programme under grant agreement No 101006799. www.takeoff-project.eu
This project has received funding from the European Union‘s Horizon 2020 research and innovation programme under grant agreement No www. eco2fuel-project.eu
06.02.2025
Advancing CO2 Capture – RWE Cutting-Edge Research for Real-World Solutions, Sandra Schmidt, RWE Power